## Slide 1: Structural Heart Live Case #1 : AM, 82 YO F
Presentation: Progressive fatigue and recurrent syncope with fall, which found to have complete heart block and elevated trans AVG
PMH: Severe AS s/p TF-TAVR with 23mmS3-1 cc in 3/2019, Hypothyroidism, HLD, non-obstructive CAD, complete heart block s/p PPM 9/2023, ICH secondary to fall 9/2023
Medications: Lisinopril, amlodipine, levothyroxine, simvastatin
Labs: Hgb 10.3, PLT 281K, K 4.4, Cr 1.04, INR 1.4
EKG: Atrial-sensed, ventricular paced rhythm
TTE: Severe aortic prosthetic stenosis (PG/MG/EOA/PV = 61/36/0.67/3.91) with minimal PVL, LVEF 70%, mild MR
Notes: 8808402

## Slide 2: Transthoracic Echocardiogram
LVEF 70%, Severely aortic prosthetic stenosis with minimal PVL
PG/MG/EOA/PV = 61/36/0.67/3.91
thickening noted of the anatomical left coronary leaflet
Notes: TTE 8/28/23
normal left ventricular size
normal left ventricular systolic function; ejection fraction (2D) = 70%
mildly increased left ventricular wall thickness
normal right ventricular size
normal right ventricular function
abnormal percutaneous aortic prosthesis (balloon-expandable: 23 mm Edwards Sapien
3) (abnormal due to stenosis); minimal paravalvular aortic regurgitation; peak velocity
= 3.91 m/s; peak gradient = 61 mmHg; mean gradient = 36 mmHg; velocity ratio = 0.23;
effective orifice area (EOA) by VTI = 0.67 cm^2
thickening noted of the anatomical left coronary leaflet
mild transvalvular aortic regurgitation
minimal valvular mitral regurgitation
mild tricuspid regurgitation
no evidence for pulmonary hypertension
no evidence for pericardial effusion

## Slide 3: Transesophageal Echocardiogram
Restricted and thickened functional noncoronary & right coronary cusps of TAVR due to valve degeneration
Notes: abnormal percutaneous aortic prosthesis (balloon-expandable: 23 mm Edwards Sapien
3) (abnormal due to stenosis, regurgitation); no evidence for paravalvular aortic
regurgitation; peak velocity = 3.34 m/s; peak gradient = 45 mmHg; mean gradient = 22
mmHg; velocity ratio = 0.22; effective orifice area (EOA) by VTI = 0.69 cm^2; EOAI =
0.47 cm^2/m^2
restricted and thickened functional noncoronary and right coronary cusps of TAVR due
to valve degeneration.

## Slide 4: Previous TAVR in 2019
23 mm Sapien3 valve – 1cc with LM protection with coronary wire
Aortic anulus
Min Ø: 20.3 mm
Max Ø: 22.2 mm
Average Ø: 21.2 mm
LM Ht 10.2
RCA Ht 12.4
Notes: VL 3.0 guide
RCA Ht 12.4
Aortic anulus
Min Ø: 20.3 mm
Max Ø: 22.2 mm
Average Ø: 21.2 mm

## Slide 5
Previous TAVR in 2019
23 mm Sapien3 valve – 1cc with LM protection with coronary wire
The top of the S3 frame is against the top of the LM
NSP
CRP
Top of S3 leaflets at Top of Commissural Tab
NSP = Neo skirt plane
CRP = Coronary risk plane

## Slide 6
Redo TAV App
Courtesy: M Fukui, V Bapat

## Slide 7
Step 1. Index TAV : S3 #23
 | Area (mm2) Diameter | Perimeter (mm)
Outflow | 353 (22*21) | 67
Waist | 304 (20*19) | 62
Inflow | 348 (22*20) | 66
Outflow
Narrowest
Inflow
Outflow
Narrowest
Inflow
Area/Perimeter measurements
Courtesy: M Fukui, V Bapat

## Slide 8: Cardiac CT Analysis Previous TAVR Inflow & Outflow: Underexpanded valve
Inflow of 23mm S3
Max: 22.0 mm
Min: 20.8 mm
Mean: 21.4 mm
Perimeter = 67.2 mm
Area = 359 mm2
Mid Frame of 23mm S3
Max: 20.7 mm
Min: 19.2 mm
Mean: 19.9 mm
Perimeter = 62.4 mm
Area = 309.3 mm2
Outflow of 23mm S3
Max: 21.8 mm
Min: 20.9 mm
Mean: 21.3 mm
Perimeter = 67.2 mm
Area = 359 mm2

## Slide 9
Redo TAV App
Courtesy: M Fukui, V Bapat

## Slide 10
Step 2. CRP and its relation to index TAV :
Bottom of RCA
at Top of commissure tab
Bottom of LCA
~ Top of commissure tab
CRP defined as below the LOWEST coronary ostia
Bottom of RCA
Bottom of LCA
This case’s CRP ~ at Top of commissure tab
Modified from: M Fukui, V Bapat

## Slide 11: Index TAV: 23 mm Sapien 3
Important landmark: Top of Commissure Tab
Top of commissure tab is where the leaflets end = Neo skirt
NSP
CRP
Modified from: M Fukui, V Bapat

## Slide 12: Cardiac CT Analysis
Narrow VTC to LCA
CRP just below NSP
NSP
CRP

## Slide 13
Redo TAV App
Courtesy: M Fukui, V Bapat

## Slide 14
Step 3. Select Second TAV
Step 4. Choose NSP and Assess relation between NSP/CRP
CRP
Near the top of commissure tab
NSP
NSP at CRP
Low risk of acute coronary obstruction
This case:
NSP and CRP nearly same level
Modified from: M Fukui, V Bapat

## Slide 15
Redo TAV App
Courtesy: M Fukui, V Bapat

## Slide 16
→ Average area: 335 mm2
Average perimeter: 65 mm
→ Second TAV
S3 #20 +1cc vs
S3 #23 -1cc?
Evolut #26
Valve size | Area (mm2) | Area derived diameter (mm)
20 | 273-345 | 18.6-21
23 | 338-430 | 20.7-23.4
26 | 430-546 | 23.4-26.4
29 | 540-683 | 26.2-29.5
IFU for S3
Step 5. Second TAV Sizing
 | Area (mm2) | Perimeter (mm)
Outflow | 353 | 67
Waist | 304 | 62
Inflow | 348 | 66
Modified from: M Fukui, V Bapat
BSA = 1.51 m2
S3 #20: 0.81 cm2/m2 (mod PPM)
S3 #23: 0.96 cm2/m2 (no PPM)

## Slide 17
Redo TAV App
Courtesy: M Fukui, V Bapat

## Slide 18
Step 6. Coronary risk assessment
CRP
Just above top of commissure tab
NSP
NSP just above CRP for LCA
Low risk of acute coronary obstruction
Delayed coronary obstruction?
Difficult coronary access post Redo TAV?
Just in case…
The level of LCA VTC = Top of stent frame
LCA VTC
Virtual circle of
#20 #23
VTC = 2.3 mm 1.5 mm
Index 23 S3 further expansion by redo TAV?
Courtesy: M Fukui, V Bapat

## Slide 19: Cardiac CT Analysis
Moderate commissural misalignment

## Slide 20: Aorto-Iliac Bifurcation

## Slide 21: Aortic Arch

## Slide 22
Planned Redo S3 Position
LM protection with guide, stent and wire above or across the index S3 outflow cell
Top of 23mm S3 just below the index S3 outflow @ ½ cell below
NSP

## Slide 23
Presentation: 82 yo F, with recent intracranial hemorrhage, severe aortic prosthetic stenosis, and potential risk of LM occlusion
TTE: severely aortic prosthetic stenosis (PG/MG/EOA/PV = 61/36/0.67/3.91) with minimal PVL, LVEF 70%, mild MR
Risk mortality : high risk for SAVR with previous TAVR for explant
Course: Patient was evaluated by heart team and recommended TF TAV-in-TAV with LM protection
Plan: TF TAV-in-TAV with a 20mm (+1 cc) Sapien3 Ultra Resilia valve after BAV (with 20mm True Balloon) via right percutaneous femoral arterial access with planned LM snorkel stent for coronary access
Summary of Case